- Files Technical specification:

  - Acceptable media file formats for Standard Definition:

PAL, resolution of picture 720x576(4X3) Or 16x9 FF (Anamorphic)

    - Format types:

      - File Container:  mov

Video Codecs: DV 25,50Mbps IMX 30, 50Mbps

Apple ProRez 422(HQ)

Audio Codec: PCM

Audio Channels: Stereo Final Mix

Sample Frequency: 48 KHz

      - File Container:  MXF

Video Codecs: DV25, 50Mbps IMX 30, 50Mbps

Audio Codec: PCM

Audio Channels: Stereo Final Mix

Sample Frequency: 48 KHz

  - Acceptable media file formats for High Definition:

Standard 1080i/50, resolution of picture 1920x1080.Display aspect ratio 16x9FF

    - Format types:

      - MXF files with compliant video essences:

XDCAM HD 4:2:2 50Mbps

DVCPRO HD 100Mbps

Audio Channels: Stereo Final Mix

Sample Frequency: 48 KHz

    - QT files with compliant video essences:

XDCAM HD 4:2:2 50Mbps

DVCPRO HD 100Mbps

APPLE ProRez 1080I (HQ)

Audio Channels: Stereo Final Mix

Sample Frequency: 48 KHz

All formats of files must be interlacing files with first upper field.

It is crucial that the source media of each file must be of good quality and that each file is accompanied by a QC report. It is important: no deinterlacing.   Files that will not meet our technical demands (due to blemishes such as digital drops, video noise, unbalanced sound levels etc') will be rejected.